## Slide 1: Fall 2024 BSCS Lecture 04 Network Performance(Delay, Loss, Throughput) and Security
National University of Computer & Emerging Sciences

## Slide 2: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 3: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 4: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 5: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 6: Caravan analogy
car ~ bit; caravan ~ packet; toll service ~ link transmission
toll booth takes 12 sec to service car (bit transmission time)
“propagate” at 100 km/hr
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka link)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
toll booth
toll booth
toll booth

## Slide 7: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 8: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 9: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 10: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
looks like delays decrease! Why?
trans-oceanic link

## Slide 11
What are the propagation time and the transmission time for a 2.5-kbyte message (an e-mail) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Example
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time. The transmission time can be ignored.

## Slide 12: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 13: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 14: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 15: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/

## Slide 16: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 17: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 18: Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Wireshark software used for our end-of-chapter labs is a (free) packet-sniffer

## Slide 19: Bad guys: fake identity
IP spoofing: injection of packet with false source address
A
B
C
src:B dest:A payload

## Slide 20: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts

## Slide 21: Lines of defense:
authentication: proving you are who you say you are
  cellular networks provides hardware identity via SIM card; no such hardware assist in traditional Internet
confidentiality: via encryption
integrity checks: digital signatures prevent/detect tampering
access restrictions: password-protected VPNs
firewalls: specialized “middleboxes” in access and core networks:
    off-by-default: filter incoming packets to restrict senders, receivers, applications
    detecting/reacting to DOS attacks
… lots more on security (throughout, Chapter 8)

## Slide 22
Computer Networking: A Top Down Approach 8th edition Jim Kurose, Keith Ross Addison-Wesley
A note on the origin of these ppt slides:
These slides are freely provided by the book authors and it represents a lot of work on their part. We would like to thank J.F Kurose and K.W. Ross.

## Slide 23: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 24: What is network security?
Confidentiality: only sender, intended receiver should “understand” message contents. Access must be restricted to those authorized to view the data in question.
  sender encrypts message
  receiver decrypts message
Authentication: sender, receiver want to confirm identity of each other
Message integrity: sender, receiver want to ensure message not altered (in transit, or afterwards) without detection
Access and Availability: services must be accessible and available to users

## Slide 25: Friends and enemies: Alice, Bob, Trudy
well-known in network security world
Bob, Alice want to communicate “securely”
Trudy (intruder) may intercept, delete, add messages
secure
sender
s
secure
receiver
channel
data, control messages
data
data
Alice
Bob
Trudy

## Slide 26: Who might Bob, Alice be?
… well, real-life Bobs and Alices!
Web browser/server for electronic transactions (e.g., on-line purchases)
on-line banking client/server
DNS servers
routers exchanging routing table updates
…

## Slide 27: Roadmap
What is network security?
Principles of cryptography
Authentication
Message integrity

## Slide 28: The language of cryptography
plaintext
plaintext
ciphertext
K
A
encryption
algorithm
decryption
algorithm
Alice’s
encryption
key
Bob’s
decryption
key
K
B

## Slide 29: Symmetric key cryptography
symmetric key crypto: Bob and Alice share same (symmetric) key: K
Q: how do Bob and Alice agree on key value?
plaintext
ciphertext
K
S
encryption
algorithm
decryption
algorithm
S
K
S
plaintext
message, m
K (m)
S
m = KS(KS(m))

## Slide 30: Symmetric key cryptography
Advantages:
Simple
Fast
Encrypt and decrypt your own files
Uses less computer resources: Single-key encryption does not require a lot of computer resources when compared to public key encryption
Disadvantages:
Need for secure channel for secret key exchange
Too many keys: A new shared key has to be generated for communication with every different party. This creates a problem with managing and ensuring the security of all these keys.
Origin and authenticity of message cannot be guaranteed: Since both sender and receiver use the same key, messages cannot be verified to have come from a particular user. This may be a problem if there is a dispute.

## Slide 31: Symmetric key crypto: DES
DES: Data Encryption Standard
US encryption standard [NIST 1993]
how secure is DES?
  DES Challenge: 56-bit-key-encrypted phrase decrypted (brute force) in less than a day
making DES more secure:
  3DES: encrypt 3 times with 3 different keys

## Slide 32: AES: Advanced Encryption Standard
New (Nov. 2001) symmetric-key NIST standard, replacing DES
Processes data in 128 bit blocks
128, 192, or 256 bit keys
Brute force decryption (try each key) takes 149 trillion years for AES

## Slide 33: Roadmap
What is network security?
Principles of cryptography
Authentication
Message integrity

## Slide 34: Authentication
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap1.0: Alice says “I am Alice”
Failure scenario??
“I am Alice”

## Slide 35: Authentication
in a network,
Bob can not “see” Alice, so Trudy simply declares
herself to be Alice
“I am Alice”
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap1.0: Alice says “I am Alice”

## Slide 36: Authentication: another try
Protocol ap2.0: Alice says “I am Alice” in an IP packet
containing her source IP address
Failure scenario??
“I am Alice”
Alice’s
IP address

## Slide 37: Authentication: another try
Trudy can create
a packet “spoofing”
Alice’s address
“I am Alice”
Alice’s
IP address
Protocol ap2.0: Alice says “I am Alice” in an IP packet
containing her source IP address

## Slide 38: Authentication: yet another try
Protocol ap3: Alice says “I am Alice” and sends her
encrypted secret password to “prove” it.
Failure scenario??
“I’m Alice”
Alice’s
IP addr
encrypted
password
OK
Alice’s
IP addr

## Slide 39: Authentication: yet another try
record
and
playback
still works!
“I’m Alice”
Alice’s
IP addr
encrypted
password
OK
Alice’s
IP addr
“I’m Alice”
Alice’s
IP addr
encrypted
password
Protocol ap3: Alice says “I am Alice” and sends her
encrypted secret password to “prove” it.

## Slide 40: Authentication: yet another try
Goal: avoid playback attack
nonce: number (R) used only once-in-a-lifetime
ap4.0: to prove Alice “live”, Bob sends Alice nonce, R. Alice
must return R, encrypted with shared secret key
“I am Alice”
R
K (R)
A-B
Alice is live, and only Alice knows key to encrypt nonce, so it must be Alice!

## Slide 41: Roadmap
What is network security?
Principles of cryptography
Authentication
Message integrity

## Slide 42: Message Integrity
Bob receives msg from Alice, wants to ensure:
message originally came from Alice
message not changed since sent by Alice

## Slide 43: Digital signatures
cryptographic technique analogous to hand-written signatures:
sender (Bob) digitally signs document, establishing he is document owner/creator.
verifiable, nonforgeable: recipient (Alice) can prove to someone that Bob, and no one else (including Alice), must have signed document

## Slide 44: Digital signatures (Asymmetric cryptography)
simple digital signature for message m:
Bob signs m by encrypting with his private key KB, creating “signed” message, KB(m)
-
-
Dear Alice
Oh, how I have missed you. I think of you all the time! …(blah blah blah)
Bob
Bob’s message, m
Public key
encryption
algorithm
Bob’s private
key
K
B
-
Bob’s message, m, signed (encrypted) with his private key
m,K
B
-
(m)

## Slide 45: Digital signatures
-
Alice thus verifies that:
  Bob signed m
  no one else signed m
non-repudiation:
  Alice can take m, and signature KB(m) to court and prove that Bob signed m
-
suppose Alice receives msg m, with signature: m, KB(m)
Alice verifies m signed by Bob by applying Bob’s public key

## Slide 46
When encrypting, you use their public key to write message and they use their private key to read it.
Asymmetric (Public-key) cryptography

## Slide 47
When signing, you use your private key to write message's signature, and they use your public key to check if it's really yours.
Digital signatures (Asymmetric cryptography) = Authentication

## Slide 48
Digital signatures (with Hashing) = Authentication + Message integrity
Bob private key
Bob public key